Compiling and running U-boot on raspberry PI 3

AIM: Compiling and building U-boot using Buildroot.

Requirements:
- Buildroot latest version
- Internet connection

Procedure:

Buildroot is a tool which automates the building of a complete Linux system(U-boot, Linux kernel image) for an embedded system, using cross-compilation, which requires a good internet connection to download the required packages.
- Download the latest Buildroot from https://buildroot.org/download.html
- Extract the tar file.
- Run ‘make menuconfig’ and select the options for Raspberry PI
(or)
Run ‘make raspberrypi3_defconfig’ for the default configuration.
Run ‘make’ without using the ‘-jN’ flag, which takes several minutes to complete.
- After completion of building, images can be found in the ‘output/images/’ directory.
- Dump the ‘sdcard.img’ file to SD card using the command ‘dd if=output/image/sdcard.img of=/dev/sdX’.

References:
- https://buildroot.org/docs.html
- buildroot-version/docs/manual/manual.pdf